ATARI 2600
Cartridge Emulation
# Introduction
This document is a quick reference of the requirements for cartridge emulation by a Microcontroller Unit (MCU) or Programmable Logic Device (PLD) such as a PLA, CPLD, or FPGA on the Atari 2600 Video Computer System.
# Console Clocks
Platform	NTSC		SECAM		PAL
IC	TIA	CPU	TIA	CPU	TIA	CPU
MHz	3.579545	1.193182	3.562500	1.187500	3.546894	1.182298

# Cartridge Slot
REAR
SGND	+5V	A8	A9	A11	A10	A12	D8	D7	D6	D5	D4
24	23	22	21	20	19	18	17	16	15	14	13

1	2	3	4	5	6	7	8	9	10	11	12
A7	A6	A5	A4	A3	A2	A1	A0	D1	D2	D3	GND
FRONT

## Pin Out
Name	Signal	Count	Cartridge Detection	Notes
Address Bus	A0 - A11	12	Input
Address Bus Cart Chip Select	A12	1	Input	The CPU A12 address line is the ROM Chip Select (CS) signal. *1 (-CS)
Data Bus	D0 - D7	8	Output (ROM), Input (RAM)
Power +5 Volts	+5V	1	Power Input
Power Ground	GND	1	Power Input
Shield Ground	SGND	1	Shield Ground	*2 (-EXROM), *3 (boot-loader)

Note:-
1. The A12 signal is sometimes labeled as -CS (active low) on some schematics. This is not the case and is the CPU A12 line. Cartridges usually contain an inverter to provide ROM IC’s with any required -CS signal.
2. The original 6-switch (heavy and light) console had a PCB footprint for an internal game ROM. The cartridge connector pin 24 is named -EXROM on some schematics. It is believed that the cartridge was to pull this line low to indicate to the console that there was an external cartridge ROM connected and to disable any internal ROM. The ROM IC footprint has been removed from later console versions. All console versions were shipped with Shield Ground (SGND); pin 24, directly connected to the Power Ground (GND); pin 12.
3. Some modern bank-switching’ cartridges appear to have used the cartridge pin 24, so when pulled high it indicates that the cartridge is to enter ‘boot loader’ mode for re-programming. This does cause issues for these carts on some remakes of the console that do not have this (SGND) connected to Power Ground (GND) within the console.
# CPU (6507)
## Missing Cartridge Signals and Special Function
There are several important control pins on the CPU that are not available on the cartridge connector. These are the R/-W (pin 26), and the ɸ0 (pin 27; input) and ɸ2 (pin 28; output) clocks. The special function is the RDY signal (pin 3).
The R/-W (pin 26) is not available and for a cartridge to determine if a read or write is being requested by the CPU, usually separate cartridge memory ranges are used to indicate this within the cartridges ROM addressable space ($1000-$1FFF). It is also theoretically possible for a cartridge to track the CPU instructions being executed to determine R/-W value.
There are no clock signals available. The address bus will need to be monitored and the relevant timings adhered to. See ‘ROM / RAM Emulation’ below for further details.
The RDY signal (pin 3) is directly connected to TIA (pin 3). This is used to stop the CPU and is requested by software by strobing the TIA register WSYNC using the assembly instruction ‘STA WSYNC’. The TIA will pause the CPU until the start of the next horizontal blank.
## Miscellaneous
The CPU only has 13 address lines. The A12 is used as a Chip Select (CS) for the cartridge. An address read by the CPU will discard the upper 3 bits. A cartridge could track the instructions and make use of the upper 3 bits to extend the ROM cartridges 4KB addressable space to 32KB addressable space or to indicate a R/-W signal. The address upper nybble values would be $1000, $3000, $5000, $7000, $9000, $B000, $D000, and $F000.
# ROM / RAM Emulation
## Memory Read Timings
Given a 1MHz CPU as reference a read is as follows. The address lines are set. This takes a ?? of ??? ns. Following detection of a change a delay of ?? ns will have to be made to allow the address lines to settle. Then the address lines will need to be read again to get the stable address. There will be ?? ns to determine the Chip Select (A12 = high), read the data byte (if CS), and set the I/O output. Then a minimum of ?? ns will pass.
## Memory Write Timings
Given a 1MHz CPU as reference a write is as follows. The address lines are set. This takes a ?? of ??? ns. Following detection of a change a delay of ?? ns will have to be made to allow the address lines to settle. Then the address lines will need to be read again to get the stable address. There will be ?? ns to determine the Chip Select (A12 = high), set the I/O as input, wait ?? ns for the data byte to settle, read the I/O data byte (if CS), and store the data byte (if CS), Then a minimum of ?? ns will pass.
## Miscellaneous Considerations
ROM emulation will need to be available upon power up reset before the Console has reset. ROM emulation reset may have to make sure the first ROM read is an actual ROM read (stable Address lines and not floating as the CPU resets – check datasheet on behaviour. If TRIS A lines CPUI and pull-up then all is okay).
## Emulation Logic
...
I/O Port TRIS / pull down (open collecttor (open drain)/ no output high)

TADS	Address Setup Time	225 ns max
TACC	Read Access Time	650 ns max
TDSU	Read Data Setup Time	100 ns min
THR	Read Data Hold Time	10 ns min

TMDS	Write Data Setup Time	20 ns min 175 ns max
THW	Write Data Hold Time	60 ns min 150 ns max

Timing Diagram

Timing Key

# References
## CPU
- 6500 Microprocessors; Commodore Semiconductor Group; NMOS; http://archive.6502.org/datasheets/mos_6500_mpu_nov_1985.pdf
- MCS-6501 – MCS6505 Microprocessor; MOS Technology Inc.; August 1975; http://retro.hansotten.nl//uploads/6502docs/MCS6501%20datasheet%20august%201975.pdf
- R650X and R651X Microprocessor (CPU); Rockwell; Rev. 8; June 1987; https://web.archive.org/web/20221112231348if_/http://archive.6502.org/datasheets/rockwell_r650x_r651x.pdf
- UM6502 / UM6507 / UM6512; 8-Bit Microprocessor; https://datasheet4u.com/pdf-down/U/M/6/UM6512_UMCCorporation.pdf
- 6502 Instruction Set; https://www.masswerk.at/6502/6502_instruction_set.html
## EPROM
- M2716; NMOS 16K (2K x 8) UV EPROM;;SGS-Thomson Microelectronics; July 1994; https://ece-classes.usc.edu/ee459/library/datasheets/2716.pdf
- 2732 32K (4K X 8) UV ERASABLE PROM; Intel; Preliminary; 9th September 1981 https://ethw.org/w/images/3/35/MEMO-data_2732.pdf
- TMS 2532; MOS LSI; 32,768 BIT ERASABLE PROGRAMMABLE READ-ONLY MEMORIES; December 1979; https://archive.org/details/2532_EPROM_Data_Sheet
## Atari 2600
- Atari 2600 Specifications; https://problemkaputt.de/2k6specs.htm
- Atari 2600 Schematics; PAL; https://www.atariage.com/2600/archives/schematics_pal/index.html
- Atari 2600 Schematics; NTSC; https://www.atariage.com/2600/archives/schematics/index.html
- Atari 2600 Schematics; https://www.retrosix.wiki/schematics-atari-2600
- Atari 2600; Console5; Wiki; https://wiki.console5.com/wiki/Atari_2600
- Atari 2600/2600A; VCS Domestic (M/N); Field Service Manual; Rev. 02; 1983; http://www.robotsandcomputers.com/computers/manuals/atari2600_fsm.pdf
# Document Information
Author:	Justin Lane	mailto:atari2600@jigglesoft.co.uk
Revision:	2025-10-09 22:48
Licence:	CC0 1.0 Universal	https://creativecommons.org/publicdomain/zero/1.0/
Location:	GitHub	https://github.com/JiggleSoft/atari2600-reference-guide