ATARI 2600
Cartridge Emulation
# Introduction
This document details the requirements for cartridge emulation by a Microcontroller Unit (MCU) or Programmable Logic Device (PLD) such as a PLA, CPLD, or FPGA on the Atari 2600 Video Computer System.
# Console Clocks
Platform	NTSC		SECAM		PAL
IC	TIA	CPU	TIA	CPU	TIA	CPU
MHz	3.579545	1.193182	3.562500	1.187500	3.546894	1.182298

# Cartridge
## PCB Slot
REAR

SGND	+5V	A8	A9	A11	A10	A12	D8	D7	D6	D5	D4
24	23	22	21	20	19	18	17	16	15	14	13

1	2	3	4	5	6	7	8	9	10	11	12
A7	A6	A5	A4	A3	A2	A1	A0	D1	D2	D3	GND

FRONT

## Pin Out
Name	Signal	Count	Cartridge Direction	Notes
Address Bus	A0 - A11	12	Input
Chip Select	A12	1	Input
Data Bus		8	Output (ROM, Input (RAM)
	+5V	1	Power Input
	GND	1
	SGND	1

# CPU (6507)

Address Lines: A0 – A11 (Cartridge Input)
Chip Select: A12 (Cartridge Input)
Data Lines: D0-D7 (Cartridge Output (ROM) and Cartridge Input (RAM)

An, CS(A12), D0, TRIS etc.

ROM Timing

Logic

References
MOS Technology Data Sheet
Rockwell Data Sheet
ROM 2712???? etc. Data Sheets

# Document Information
Author:	Justin Lane (atari2600@jigglesoft.co.uk)